Pinhole Camera

Mrs. McArthur

Materials

5- 5in x 5in squares of Mat Board

5- 5 1/8 in x 5 1/8 squares of Mat Board

1- 2 in x 2in Metal Tin (pop can or cooking tin)

Masking Tape

Black Paint

Electrical Tape

Push Pin

Photo Paper- 5 in x 4 in

Directions

- In one of the 5 1/8 in x 5 1/8 in boxes, cut a 1 inch by 1 inch whole in the center.

- Masking Tape the corners of all the 5 in by 5 inch boxes together, so that they make a box with no top. Make sure that the box with the whole cut out from step 1 is at the bottom. Set aside.

- Assemble the 5 in x 5 in boxes in the same manner as step 2. Set aside.

- Using ink or paint, paint the inside and outsides of the mat board boxes. Be sure to cover everything even the masking tape. Set aside to dry.

- Once dry use black electrical tape to go over masking tape sides.

- Using Electrical Tape, tape 2 in x 2in metal square to the outside of the bigger box over the 1 in x 1in hole. Be sure to electrical tape everything but a little slip on top of the box.

- Now create a “shutter” by using 2 pieces of tape. One will go over the slip you left open from step 6 fold over the end of the tape a little so you pull the tape back easily. The other piece goes at the other end (not folded end) of the last piece you laid down to secure it. Now you should have a working flap.

- On the bottom of the 5 in box create pulls to open box. This is done by using electrical tape folded almost in half on itself. Leave ends of tape free to attach to bottom of box.

- In darkroom, cut a piece of photo paper into 5 in x 4 in piece, using masking tape in a loop attach to back of photo paper. Attach photo paper to back of box.

- Put box together, make sure “shutter” is closed.

- Get ready to take picture(